# Linear Quadratic Gaussian Integral(LQGI)
This controller works for the most cases. It’s a standard controller for simple problems such as temperature control, water level control, electrical DC motor control etc. You should choose this controller if you have:
- No disturbances is effecting the system
- No reference model following is required
- The control object is temperature system, electrical or fluid system.
Here is a step by step to create the infinite horizon LQGI controller:
1. Start to estimate your discrete state space model. Select the OKID, MOESP or N4SID methods to get the estimated model.
  alignl dot x( k+1 ) = Ax(k) + Bu( k) newline alignl y(k) = Cx(k) + Du(k) + w( k )
2. Start to solving Discrete Algebraic Riccati Equation(DARE) by iterating it like 100 times:
  alignl X(k+1) = AX(k)A^T - ({A^T}X(k){C^T})(R + CX(k)C^T)^{-1}(CX(k)A^T) + Q
  Where w( k ) is the measured steady state noise vector from a sensor or sensors and:
  alignl Q = I newline alignl R = E lbrace w(k)w^T (k) rbrace newline alignl X( 0 ) = 0
3. After solving DARE, then find the steady state Kalman gain matrix K
  K=(CX(k)C^T + R)^{-1}(CX(k)A^T)
4. Now create the augmented state space model with integral action.
  alignl left [ matrix{x(k+1) ## x_i(k+1)} right ] = {left[matrix{A # 0 ## -C # 1 } right]} underbrace { circle A }left[matrix{x(k) ## x_i(k) } right] + {left[matrix{B ## -D } right]} underbrace { circle B } u(k) + left[matrix{0 ## 1 } right] r( k) newline alignl y( k ) = {left[matrix{C # 0 } right]} underbrace { circle C }left[matrix{x(k) ## x_i(k) } right] + D u(k)
5. Start solving another DARE by iterating it like 100 times.
  alignl X(k+1) = circle A^T X(k) circle A -( circle A^T X(k) circle B)(R + circle B^T X(k) circle B)^{-1}(circle B^T X(k) circle A) + Q
  With:
  alignl Q = I newline alignl R = %rho I , %rho > 0 newline alignl X( 0 ) = 0
6. After have solve that DARE, then find the control law and integral law:
  left[ matrix{L # L_i }right] =(circle B^T X(k) circle B + R)^{-1}(circle B^T X(k) circle A)
Now we have found our Kalman gain matrix K and the control law L and the integral law L_i Now it’s time to create the LQGI controller:
1. Set the initial state vector x(k) = 0, x_i(k) = 0, k= 0 , and your reference r( k ) to your desire value.
2. Measure with your sensor or sensors the output signal y_m( k )
3. Compute the control law
  u( k ) = K_f r(k) - ( Lx(k) - L_i x_i(k) )
  And update the integral law.
  x_i( k+1 ) = x_i( k ) + r( k ) - y_m( k )
  K_r is a reference gain where q is an integral pole. It will make the integral action slower 0 <- q or faster q -> 1 .
  K_f = L_i over { 1-q }, 0 <= q < 1
4. Then compute the estimated state from the Kalman filter.
  x(k+1) = (A -KC)x( k ) + Bu( k ) + Ky_m( k )
Now repeat the following to control the object with the LQGI controller:
1. u( k ) = K_f r - ( Lx(k) - L_i x_i(k) ) - Control
2. x_i( k+1 ) = x_i( k ) + r( k ) - y_m( k ) - Integrate
3. x(k+1) = (A -KC)x( k ) + Bu( k ) + Ky_m( k ) - Estimate
Practical methods:
- Saturation on u( k )
- Anti-windup on x_i( k )